## Slide 1
ASSIGNMENT 10
Alamouti Coding Scheme Implementation

## Slide 2
Wireless channels suffer from multipath fading, which degrades signal reliability.
The Challenge:
How to achieve Transmit Diversity without increasing bandwidth or requiring feedback from the receiver?
Implement and verify the Alamouti Space-Time Block Code (STBC) for 2 Transmit and 1 Receive antenna (2x1).
Compare its performance against standard MISO transmission.
•
•
•
Problem Statement

## Slide 3
Develop MATLAB code for Alamouti STBC.
Implement modulation schemes:
Simulate over a Rayleigh Fading Channel.
Plot Bit Error Rate (BER) vs SNR (0-20 dB).
Compare STBC 2x1 performance with standard MISO 2x1.
•
•
•
•
•
BPSK (Binary Phase Shift Keying)
QPSK (Quadrature Phase Shift Keying)
•
•
Objectives
1. Implementation
2. Analysis

## Slide 4
System Architecture: Alamouti 2x1
Space-Time Coding Matrix

## Slide 5
(Random Generation)
(Alamouti Matrix Construction)
(Rayleigh Fading + AWGN)
Data Flow Diagram (DFD)

## Slide 6
% 4. Combining Scheme
% 5. Decoding
Symbol Pair: Takes two symbols (s_1, s_2) at a time.
Orthogonality: The received signals r_1 and r_2 are linear combinations of transmitted symbols.
Decoupling: By using the channel estimates (h_1, h_2), we can perfectly separate s_1 and s_2 without interference.
•
•
•
Pseudocode: BPSK Implementation
Explanation
Initialize N bits
Map bits → BPSK symbols
Split symbols into s1, s2
Form Alamouti matrix S
For each SNR:
Compute noise variance N0
Generate Rayleigh channels h1, h2
Generate noise n1, n2
% ----- STBC Transmission -----
r1 = h1*s1 − h2*conj(s2) + n1
r2 = h1*s2 + h2*conj(s1) + n2
Decode:
s1_hat = (h1*conj(r1) + h2*conj(r2)) / (|h1|² + |h2|²)
s2_hat = (-h2*conj(r1) + h1*conj(r2)) / (|h1|² + |h2|²)
Decide bits and compute BER_STBC
% ----- MISO (2 Tx, no STBC) -----
Generate h1m, h2m
r = (h1m + h2m)*s + n
s_hat = r / (h1m + h2m)
Detect bits and compute BER_MISO
BPSK STBC vs MISO

## Slide 7
% 3. Decoding (Real & Imaginary)
% 4. Bit Reconstruction
Complex Symbols: QPSK carries 2 bits per symbol (In-phase and Quadrature).
Normalization: Power is normalized by sqrt{2}.
Detection: Since QPSK uses both real and imaginary axes, threshold detection is applied to both components independently.
•
•
•
Pseudocode: QPSK Implementation
Explanation
Initialize N bits
Group bits → I,Q → QPSK symbols
Split symbols into s1, s2
Form Alamouti STBC matrix
For each SNR:
Compute noise power N0
Generate channels h1, h2
Generate noise n1, n2
% ----- STBC Transmission -----
r1 = h1*s1 + h2*s2 + n1
r2 = -h1*conj(s2) + h2*conj(s1) + n2
Decode:
s1_hat = (conj(h1)*r1 + h2*conj(r2)) / (|h1|² + |h2|²)
s2_hat = (conj(h2)*r1 - h1*conj(r2)) / (|h1|² + |h2|²)
Recover bits and compute BER_STBC
% ----- MISO (No STBC) -----
Generate h1m, h2m
r = (h1m + h2m)*s + noise
s_hat = r / (h1m + h2m)
Detect I,Q bits
Compute BER_MISO
QPSK STBC vs MISO

## Slide 8
Process Workflow

## Slide 9
STBC 2x1 (Alamouti): Shows significant improvement in BER at higher SNR values compared to the standard MISO channel.
The diversity gain effectively steepens the BER slope.
At 10dB SNR, BER drops to approx 10^{-3}.
•
•
•
Results: BPSK Performance
Observation

## Slide 10
Similar diversity gain trends observed as BPSK.
However, QPSK requires higher SNR (~3dB more) to achieve the same BER as BPSK due to denser constellation.
The Alamouti scheme successfully provides full spatial diversity order of 2 for 2 transmit antennas.
It mitigates fading effects without bandwidth expansion.
•
•
•
•
Results: QPSK & Conclusion
QPSK Analysis
Conclusion