## Slide 1
WIRELESS COMMUNICATIONS • ASSIGNMENT 4
Rician Fading & Jakes Spectrum

## Slide 2
1. Rician Flat-Fading Model
What is it?
Rician fading occurs when there is a dominant Line-of-Sight (LOS) component alongside multipath scattering. It is common in satellite links or open environments.
The K-Factor
The ratio of LOS power to scattered power.
Envelope Calculation
The received envelope r is the magnitude of this complex signal.
•
K = 0: No LOS. Reduces to Rayleigh Fading.
•
K = ∞: Pure LOS. No Fading (Gaussian channel).
Signal = (g1 + g2•X) + j(g1 + g2•Y)
Where X, Y are Gaussian Random Variables

## Slide 3
[0, 3, 7, 12, 15]
Gaussian X, Y
r = |Signal|
Compare with Theory
Data Flow: Rician Simulation

## Slide 4
Pseudo Code: Rician Fading
Humanized Explanation
Why calculate g1 & g2? The total energy must remain 1. As 'K' increases, we allocate more energy to the direct path (g1) and less to the scattered path (g2).
The 'Loop' Logic: We repeat the experiment for different K values to visualize how the probability density function (PDF) shifts shape.
START
SET K_values = [0, 3, 7, 12, 15]
SET N = 100000
SET Omega = 1
SET r_axis = linspace(0, 3)
FOR each K in K_values:
COMPUTE g1 = sqrt( K / (2 * (K + 1)) ) // LOS component
COMPUTE g2 = sqrt( 1 / (2 * (K + 1)) ) // Scattered component
GENERATE X = random Gaussian samples of size N
GENERATE Y = random Gaussian samples of size N
// Generate Rician envelope (practical)
COMPUTE r = sqrt( (g1 + g2*X)^2 + (g1 + g2*Y)^2 )
// Compute theoretical PDF
FOR each value in r_axis:
COMPUTE pdf = (2*(K+1)/Omega) * r_axis *
exp( -(K+1)/Omega * r_axis^2 - K ) *
BesselI0( 2 * r_axis * sqrt(K*(K+1)) / Omega )
END FOR
PLOT histogram of r
OVERLAY theoretical PDF curve
END FOR
END

## Slide 5
Rician Simulation Results
Key Observations
•
K = 0 (Rayleigh): The graph is skewed left. It has no dominant component.
•
K = 7 to 15: As K increases, the graph becomes a symmetrical "bell curve" (Gaussian).
•
Shift: The peak moves to the right (around 1.0) as the signal becomes stable and less random.

## Slide 6
2. Jakes Spectrum & Autocorrelation
The Concept
When a receiver moves through a multipath environment, the received frequency shifts due to the Doppler Effect.
Jakes model describes the power spectral density (PSD) of this fading channel.
The "U" Shape
The PSD is maximum at ± f max (moving directly towards/away from the source) and minimum at 0 Hz (moving perpendicular).
Power Spectral Density S(f):

## Slide 8
// 1. Define Frequency Range
// Go slightly beyond fmax
// 2. Calculate PSD (The U-Shape)
FOR EACH
IN
IF
// Apply Jakes Formula
ELSE
END IF
END LOOP
// 3. Calculate Autocorrelation
// Theoretical formula using Bessel Function
Pseudo Code: Jakes Spectrum
Logic Explanation
The Mask: In the code, we use a condition abs(f) < fmax. This is because the signal only exists within the Doppler shift limits. Outside this range, the power is zero.
Autocorrelation: The code uses besselj(0, ...). This mathematical function perfectly describes how the correlation of the signal ripples and fades over time delay (tau).
START
SET fmax = 100
SET sigma2 = 1
// Frequency axis
SET f = linspace( -1.2*fmax , 1.2*fmax )
INITIALIZE PSD array S of same size as f
FOR each frequency value f_i in f:
IF |f_i| < fmax THEN
COMPUTE S[i] = sigma2 / ( pi * fmax * sqrt( 1 - (f_i/fmax)^2 ) )
ELSE
SET S[i] = 0
END IF
END FOR
PLOT S vs f // Jakes Doppler spectrum
// Autocorrelation function
SET tau = linspace( -0.05 , 0.05 )
FOR each tau_i in tau:
COMPUTE R[i] = sigma2 * BesselJ0( 2 * pi * fmax * tau_i )
END FOR
PLOT R vs tau // Jakes autocorrelation function
END

## Slide 9
Jakes Model Results
1. Power Spectral Density
Sharp peaks at edges (-100, 100 Hz). This is the classic "Bathtub" or "U" shape.
2. Autocorrelation R(τ)
A Bessel function (Sinc-like). Shows how quickly the channel changes.

## Slide 10
Summary
Rician Fading
Models environments with a clear Line-of-Sight. The K-factor determines if the channel behaves like Rayleigh (Chaotic) or Gaussian (Stable).
Jakes Spectrum
Models the frequency shift caused by motion. The U-shaped PSD proves that most energy arrives at the maximum Doppler shift.