## Slide 1
ASSIGNMENT 6
Channel Capacity Optimization: Water-filling Algorithm

## Slide 2
In a frequency-selective fading channel, signal attenuation varies across different subchannels.
The Goal:
Develop a MATLAB simulation to maximize the total capacity of a wireless channel.
Implement the Water-filling Algorithm for optimal power allocation.
Distribute a fixed power budget ($P_t$) across $N$ subchannels based on their channel gains ($|h|^2$).
Maximize Rate vs Power Constraint
•
•
•
Problem Statement
Optimal Allocation

## Slide 3
Simulate a Rayleigh fading channel with multiple subchannels.
Compute the "Water Level" (mu) derived from Lagrange multipliers.
Compare Water-filling (Optimal) vs Uniform Power Allocation (Equal power to all).
Analyze the Spectral Efficiency (bits/s/Hz).
•
•
•
•
Objectives
1. Implementation
2. Comparison

## Slide 4
($N_{ch}, P_t, N_0$)
(Calc Gains g, Sort Descending)
(Find mu, Allocate P_i)
(Capacity, Plots)
Data Flow Diagram (DFD)

## Slide 5
Initialize system parameters and generate random Rayleigh fading coefficients. Compute channel-to-noise ratios (CNR).
% 3. Sort Gains (Descending)
% Critical for finding cutoff threshold
Generate complex Gaussian h.
Compute power gain g = |h|^2.
Sort gains to simplify the water-filling logic (Strongest first).
•
•
•
Pseudocode: Initialization
Step 1: Channel Setup
% 1. Initialize Parameters
Nch = 6;
Pt = 5;
N0 = 1;
% 2. Generate Channel Gains
h = (randn(1, Nch) + 1j*randn(1, Nch)) / sqrt(2);
g = abs(h).^2;
% 3. Sort Gains (Descending)
% Critical for finding cutoff threshold
[g_sorted, idx] = sort(g/N0, 'descend');

## Slide 6
a
IF
% Found cutoff k
END IF
END FOR
% 5. Allocate Power
FOR
END FOR
% 6. Calculate Total Capacity
Pseudocode: The Waterfilling Algorithm
% 4. Iterative Water Level Finding
FOR k = 1 to Nch:
% Calculate potential water level mu
mu = (Pt + sum(1 ./ g_sorted(1:k))) / k;
% Check if next channel is too weak
IF (k < Nch) AND (mu <= 1/g_sorted(k+1)):
BREAK loop; % Found cutoff k
END IF
END FOR
% 5. Allocate Power
P_opt = zeros(1, Nch);
FOR i = 1 to k:
P_opt(idx(i)) = mu - 1/g_sorted(i);
END FOR
% 6. Calculate Total Capacity
C = sum(log2(1 + P_opt .* g / N0));

## Slide 7
Start
Set number of channels Nch
Set total power Pt and noise N0
Generate Rayleigh fading channel h
Compute power gains g = |h|²
--- Uniform Allocation ---
Divide total power equally across channels
Compute uniform capacity
--- Water-Filling Allocation ---
Sort channel gains in descending order
Find water level μ using iterative condition
Compute optimal power P_opt = μ − 1/g for active channels
Compute water-filling capacity
Display cutoff SNR, optimal power, capacities
Plot water-filling vs uniform power levels
Plot water level line
Plot bar chart comparing capacities
End
Comparison between Uniformly Distributed and Waterfilling Pseudocode:

## Slide 8
Process Workflow

## Slide 9
As seen in the simulation output:
Strong channels received significantly more power (e.g., 1.6W, 1.36W).
Weak channels (Index 3 and 4) received 0 Watts because their inverse gain was above the water level.
Cutoff SNR (1/\mu): Calculated as ~0.4612.
•
•
•
Simulation Results
1. Power Allocation

## Slide 11
Method | Capacity (bits/s/Hz)
Water-filling | 5.4176
Uniform Allocation | 4.5859
The Water-filling algorithm successfully maximizes theoretical capacity.
By sacrificing weak channels, we gain significant throughput in strong channels.
It outperforms uniform allocation by approx 18% in this scenario.
•
•
•
Comparison & Conclusion
Capacity Comparison
Conclusion

## Slide 12
This algorithm is foundational for modern systems. Future enhancements include:
MIMO Systems: Applying water-filling to spatial eigenmodes (Singular Value Decomposition).
OFDM: Used in 4G/5G to allocate power across thousands of subcarriers.
Real-time CSI: Adapting to fast-changing Channel State Information in high-mobility scenarios.
•
•
•
Future Scope