## Slide 1
ASSIGNMENT 7
MIMO Channel Capacity & BER Analysis

## Slide 2
Modern wireless systems demand higher data rates and reliability without increasing bandwidth.
Key Challenges:
This study investigates how Multiple-Input Multiple-Output (MIMO) technology enhances capacity and how diversity improves BER.
Fading channels degrade signal quality.
Single antenna systems (SISO) have limited capacity limits.
Bit Error Rate (BER) increases in deep fading conditions.
•
•
•
Problem Statement

## Slide 3
Simulate and compare Channel Capacity for:
Simulate Bit Error Rate (BER) for BPSK modulation.
Analyze performance over a Rayleigh Fading channel.
Verify simulation results against theoretical bounds.
•
•
•
•
SISO (1x1)
SIMO (1x2)
MISO (2x1)
MIMO (2x2)
•
•
•
•
Objectives
1. Capacity Analysis
2. Error Performance

## Slide 4
...
Baseline reference
...
Receive Diversity
...
Transmit Diversity
...
Spatial Multiplexing
System Architecture Overview
SISO (1x1)
SIMO (1x2)
MISO (2x1)
MIMO (2x2)

## Slide 5
(0 - 40 dB)
(Rayleigh H Matrix)
SISO SIMO 2*1 MISO 1*2 MIMO 2*2

## Slide 6
% SISO Capacity
% MIMO Capacity Formula
% C = log2( det( I + (SNR/Nt) * H * H' ) )
% Average over samples
END
Channel H: Complex Gaussian random variables representing Rayleigh fading.
Determinant: The core of MIMO capacity. The eigenvalues of HH^H determine the parallel spatial pipes available.
Averaging: Monte Carlo simulation (10,000+ runs) is used to find the ergodic capacity.
•
•
•
Pseudocode: MIMO Capacity
Logic Explanation
% 1. Define SNR Range
Pt_dB = 0:5:40;
Pt = 10^(Pt_dB/10);
% 2. Iterate for Monte Carlo
FOR k = 1:length(Pt)
% Generate Rayleigh Channel Matrix
H = (randn(Nr, Nt) + 1j*randn(Nr, Nt))/sqrt(2);
% SISO Capacity
T1 = log2(1 + g * Pt(k));
% MIMO Capacity Formula
% C = log2( det( I + (SNR/Nt) * H * H' ) )
inner = eye(Nr) + (Pt(k)/Nt) * (H * H');
C_inst = log2( det(inner) );
% Average over samples
Capacity(k) = mean(C_inst);
END
START
-------------------------------------------------
1. SISO CAPACITY (1×1)
-------------------------------------------------
Define SNR range Pt_dB = 0 to 40 step 5
Convert Pt_dB → Pt (linear scale)
Generate Rayleigh channel h
Compute power gain g = abs(h)^2
For each SNR value:
Compute T1 = log2(1 + g * Pt)
-------------------------------------------------
2. SIMO CAPACITY (1×2)
-------------------------------------------------
Generate Rayleigh channels h1 and h2
Compute total gain h2_total = abs(h1)^2 + abs(h2)^2
For each SNR value:
Compute instantaneous capacity C = log2(1 + Pt * h2_total)
Average over all samples → T2

## Slide 7
-------------------------------------------------
3. MISO CAPACITY (2×1) – MRT
-------------------------------------------------
Set Nt = 2
Generate Rayleigh channels h1 and h2
Compute MRT gain h_total = abs(h1)^2 + abs(h2)^2
For each SNR value:
Compute T3 = mean( log2(1 + (Pt/Nt) * h_total) )
-------------------------------------------------
4. MIMO CAPACITY (2×2)
-------------------------------------------------
Set Nt = 2, Nr = 2
Define number of iterations
For each SNR value Pt(k):
Initialize sumC = 0
Repeat for many channel realizations:
Generate 2×2 Rayleigh channel matrix H
Compute C_inst = log2( det( I + (Pt/Nt) * H * H' ) )
Add to sumC
Compute T4(k) = sumC / number_of_samples

## Slide 8
% 3. Detection (MRC)
% 4. Error Counting
BPSK Symbols: Generated as -1 and +1.
Noise: Added as AWGN (Complex Gaussian).
MRC Detection: Maximum Ratio Combining. We multiply the received signal y by the conjugate of the channel h^ to align phases and maximize SNR.
•
•
•
Pseudocode: BER Analysis
Logic Explanation
% 1. Generate Symbols
s = 2*randi([0 1], 1, N) - 1;
% 2. Channel & Noise
h = (randn + 1j*randn)/sqrt(2);
n = sqrt(N0/2)*(randn + 1j*randn);
y = h * s + n;
% 3. Detection (MRC)
y_mrc = real( conj(h) * y );
detected_bits = (y_mrc >= 0);
% 4. Error Counting
BER = sum(detected_bits != sent_bits) / N;

## Slide 9
MIMO (2x2): Highest capacity. Slope increases linearly with min(Nt, Nr).
SIMO (1x2): Better than SISO due to logarithmic array gain.
SISO (1x1): Lowest capacity baseline.
Simulation perfectly matches theoretical Rayleigh curve.
BER decreases linearly (on log scale) as SNR increases.
•
•
•
•
•
Results & Conclusion
Capacity Results
BER Results