## Slide 1
ASSIGNMENT 8
Diversity Techniques Analysis: SC, EGC, and MRC

## Slide 2
Wireless channels suffer from multipath fading, where signal strength fluctuates randomly, leading to high Bit Error Rates (BER).
The Solution?
Diversity techniques use multiple antennas to improve reliability. This study analyzes how different combining methods mitigate fading effects in a SIMO (Single-Input Multiple-Output) system.
Deep fades cause data loss
Problem Statement
Signal Fading

## Slide 3
Selection Combining: Choosing the strongest signal path.
Equal Gain Combining: Phase alignment and equal weighting.
Maximal Ratio Combining: Optimal weighting based on SNR.
Objectives
Implement SC
Implement EGC
Implement MRC

## Slide 4
1x2 Diversity System
Modulation: BPSK (Binary Phase Shift Keying)
Channel: Rayleigh Fading (Complex Gaussian)
Configuration: SIMO (1 Tx, 2 Rx antennas)
Noise: AWGN (Additive White Gaussian Noise)
Samples: 10^5 bits for statistical accuracy
•
•
•
•
•
Tx (1)
Rx 1
Rx 2
System Architecture Overview
Simulation Parameters

## Slide 5
(Random Gen)
(BPSK)
(Rayleigh + AWGN)
(SC / EGC / MRC)
Data Flow Diagram (DFD)

## Slide 6
% 3. Select signal from that branch
FOR
% Co-phase and normalize
END
% 4. Detection
Logic: Monitor the SNR of all diversity branches.
Selection: At any instant, the receiver processes only the signal from the antenna with the highest instantaneous SNR.
Pros/Cons: Simplest to implement but discards useful energy from other branches.
•
•
•
Pseudocode: Selection Combining (SC)
Explanation
START
Set number of bits N
Set number of diversity branches L = 2
Define SNR range EbN0_dB
Initialize BER arrays:
BER_SC
BER_EGC
BER_MRC
FOR each SNR value in EbN0_dB:
Convert SNR from dB → linear (EbN0)
Compute noise variance N0 = 1 / EbN0
Generate random BPSK bits tx
Map to symbols s = 2*tx – 1
Generate Rayleigh fading matrix h of size L × N
Generate AWGN noise n of size L × N
Compute received signals r = h*s + n
--------------------------------------------------------
SELECTION COMBINING (SC)
--------------------------------------------------------
Compute branch SNRs snr_branch = abs(h)^2 / N0
For each bit find best branch index idx_max
For each k:
y_SC(k) = conj(h_selected) * r_selected / abs(h_selected)
Detect rx_SC = sign(real(y_SC))
Compute BER_SC

## Slide 7
% 2. Summation
% Sum all aligned branches equally
% 3. Detection
% 4. Error Calculation
Logic: Utilize signals from all branches.
Phase Alignment: The phase shift introduced by the channel is removed (co-phasing) so signals add constructively.
Weighting: All branches are given equal weight (unlike MRC).
•
•
•
Pseudocode: Equal Gain Combining (EGC)
Explanation
--------------------------------------------------------
EQUAL GAIN COMBINING (EGC)
--------------------------------------------------------
Phase-align signals: r_egc = sum( r * exp(-j*angle(h)) )
Detect rx_EGC = sign(real(r_egc))
Compute BER_EGC

## Slide 8
% AND removes phase shift simultaneously
% 3. Detection
% 4. Error Calculation
Logic: Optimal linear combining technique.
Weighting: Branches are weighted proportional to their signal amplitude. Strong signals contribute more; weak/noisy signals contribute less.
Result: Maximizes the output SNR.
•
•
•
Pseudocode: Maximal Ratio Combining (MRC)
Explanation
--------------------------------------------------------
MAXIMAL RATIO COMBINING (MRC)
--------------------------------------------------------
Compute weighted sum r_mrc = sum( conj(h) * (h*s + n) )
Detect rx_MRC = sign(real(r_mrc))
Compute BER_MRC
END FOR
Plot all BER curves (SC, EGC, MRC)
Compute difference between EGC and MRC
END

## Slide 9
MRC (Best): Lowest BER curve. Maximizes SNR.
EGC (Middle): Very close performance to MRC (~1.4e-3 diff).
SC (Worst): Requires higher SNR to achieve same BER.
•
•
•
Results: BER Comparison
Performance Hierarchy

## Slide 10
EGC vs MRC Comparison
For equal noise variance branches, EGC and MRC perform very similarly.
MRC penalizes noisy branches by assigning them smaller weights (|h|). EGC treats noise in weak branches the same as strong branches, slightly degrading performance.
Results: Data Analysis
Why is MRC better?

## Slide 11
Diversity techniques significantly lower BER in fading channels.
MRC is the optimal combiner but requires estimating channel amplitude and phase (High complexity).
EGC offers a good trade-off, needing only phase estimation.
SC is simplest but least efficient.
MIMO Systems: Extending diversity to both Transmit and Receive sides (Tx/Rx Diversity).
Correlated Fading: Analyzing performance when antennas are close together (correlation > 0).
Real-time Implementation: Testing on FPGA or SDR (Software Defined Radio).
•
•
•
•
•
•
•
Conclusion & Future Scope
Conclusion
Future Scope